## Slide 1
Lab Book 2.0. Couplers
Student: Hugo Beltrán Sanz

## Slide 2: Instructions General
SCRIPTS
From GitHub -> Fork the repo: https://github.com/cccanvas-upv/cifoin-lab2.git
Clone the repo using VSCode
Terminal: uv sync
Run the Jupyter Notebook: COUPLERS_Student.ipynb
Cross-Sections to be studied:
h
(height)
w (width)
Core
Cladding
w (width)
MMI Body
Cladding
Multimode Interference (MMI) coupler
Directional coupler (DC)
Core
g
(gap)
h
(height)

## Slide 3
Directional coupler

## Slide 4: Learning outcome #1 - Directional coupler cross-section in GDSFactory
n_eff: TE even/odd = 1.609425 / 1.601166; TM even/odd = 1.535403 / 1.520573.
TE fraction is ~0.995 for modes 0-1 and TM fraction is ~0.99 for modes 2-3.
Lpi_TE = 93.84 um and Lpi_TM = 52.26 um, so the coupling length is polarization dependent.

## Slide 5: Learning outcome #2 - Directional coupler length and coupling coefficient Wavelength 1.5 um - width 1.2 um - gap 0.6 um - thickness 300 nm
At lambda = 1.50 um, the deep directional coupler gives Lpi_TE = 118.67 um and L_50/50 = 59.34 um.
The normalized response is K = sin^2(pi L / 2 Lpi): 50/50 at L/Lpi = 0.5 and complete transfer at L/Lpi = 1.

## Slide 6: Learning outcome #3 - 2x2 Directional Coupler Wavelength 1.55 um - gap sweep 0.2 to 1.2 um
Gap sweep Lpi [um]: 0.2->25.81, 0.4->50.11, 0.6->94.03, 0.8->173.96, 1.0->318.88, 1.2->580.43.
For gap = 0.6 um: L_50/50 = 47.01 um, ratio = 0.500/0.500 and EL = 0.135 dB. Larger gap reduces evanescent coupling and increases Lpi; EL is not monotonic in this EME sweep.

## Slide 7: Learning outcome #4 - Parallel uncoupled waveguides - TE0 mode Wavelength 1.55 um, width 1.0 um, L = 10 mm
deep waveguide
e vs gap for 10 mm wvgs to be uncoupled
shallow waveguide
slab_thickness = 150 nm
e vs gap for 10 mm wvgs to be uncoupled
First sampled K<0.01 points can be periodic recurrences for exactly 10 mm, so they are reported but not used as the final layout rule.
Conservative criterion: invert K = sin^2(pi L / 2 Lpi) and require Lpi > 156.8 mm; selected gaps are deep = 4.0 um and shallow = 5.0 um.

## Slide 8
Multimode Interferometer (MMI) Coupler

## Slide 9: Learning outcome #5 - Multimode Interference (MMI) Coupler cross-section
For W_MMI = 12 um, first TE-like modes: n_eff = 1.678660 and 1.675127. First TM-like modes: n_eff = 1.577421 and 1.573889.
Lpi_TE = 219.41 um and Lpi_TM = 219.48 um. The deep MMI body is almost polarization matched for this width, but not exactly identical.

## Slide 10: Learning outcome #6.1 - 2x2 Multimode Interference Coupler Wavelength 1.55 um, wMMI = 6.6 um
Baseline: L = 0.5 Lpi = 34.52 um, I/O at +/- W/6. Total OUT power = 0.9075, EL = 0.4217 dB, ratio = 0.5152/0.4848.
Compared with the DC 50/50 case at gap = 0.6 um, the MMI is shorter (34.52 um vs 47.01 um), but its baseline excess loss is higher before optimization.
Imbalance is about 3.0 percentage points, so this is a useful starting point but needs optimization.

## Slide 11: Learning outcome #6.2 - 2x2 Multimode Interference Coupler Optimization Wavelength 1.55 um, wMMI = 6.6 um
Manual optimization: dy = 0.07 um and dL = -0.8 um with 1.0 um I/O width. Total OUT power = 0.9076, EL = 0.4210 dB.
Output ratio improves to 0.5003/0.4997; loss remains similar because mode overlap has not been improved.

## Slide 12: Learning outcome #6.3 - 2x2 MMI Optimization with wider I/O Wavelength 1.55 um, wMMI = 6.6 um
I/O total width = 2.0 um (wg_width_dw = 1.0 um), dy = 0.05 um and dL = +0.2 um.
Total OUT power = 0.9924, EL = 0.0332 dB and ratio = 0.4996/0.5004. This meets the 50/50 and <0.1 dB targets.

## Slide 13: Learning outcome #7 - 1x4 Multimode Interference Coupler Wavelength 1.55 um, wMMI = 6.5 um
Mini-sweep selected W = 6.5 um, scale = 1.04, dL = +0.6 um. Lpi = 67.05 um and total length = 13.17 um.
Total OUT power = 0.9573, EL = 0.1895 dB, ratios = 0.2470/0.2530/0.2531/0.2469. This improves loss versus the previous equal-split design while keeping imbalance below 0.31 percentage points.

## Slide 14: Extra #1 - Directional coupler gap dependence Wavelength 1.55 um, width 1.0 um, gap 0.2-2.4 um
deep waveguide
e vs gap for TE and TM
shallow waveguide
e vs gap for TE and TM
Curves: deep TE, deep TM, shallow TE, shallow TM.
Lpi generally rises quickly with gap because the evanescent overlap decreases.
At gap = 0.6 um: deep TE/TM = 58.77/38.43 um; shallow TE/TM = 39.25/33.86 um.
The TM and slab behavior differs strongly at large gap.

## Slide 15: Extra #2 - Directional coupler wavelength dependence Wavelengths 1.5-1.7 um, gap = 0.6 um, width 1.0 um
deep waveguide
e vs wvl for TE and TM
shallow waveguide
e vs wvl for TE and TM
Relative Lpi change from 1.5 to 1.7 um:
deep TE = -44.0%, deep TM = -25.0%
shallow TE = -22.1%, shallow TM = -10.2%
Directional couplers are wavelength sensitive, especially the deep TE case.

## Slide 16: Extra #3 - MMI coupler wavelength dependence Wavelengths 1.5-1.7 um, wMMI = 6.6 um
deep waveguide
e vs wvl for TE and TM
shallow waveguide
e vs wvl for TE and TM
MMI relative Lpi change:
deep TE/TM = -11.5% / -8.0%
shallow TE/TM = -9.9% / -7.1%
For the same slab and polarization, the MMI varies less than the directional coupler in Extra #2.

## Slide 17: Extra #4 - MMI body width dependence Wavelength 1.55 um, wMMI = 5-10 um
deep waveguide
e vs width for TE and TM
shallow waveguide
e vs width for TE and TM
Polarization-independent point?
No exact TE/TM match was found in the sampled widths.
Closest sampled point for both deep and shallow: W = 10.0 um.
TE/TM Lpi difference: deep = 1.07%, shallow = 0.58%. Further fine tuning would be needed.

## Slide 18: Thank you